## Slide 1
A soil is composed primarily of minerals which are produced from parent material that is weathered or broken into small pieces.
Plants and animals have important roles to play in soil.
The term "soil" can have different meanings, depending upon the field in which it is considered.
To a geologist, it is the material in the relative thin zone of the Earth's surface within which roots occur, and which are formed as the products of past surface processes.
To a pedologist, it is the substance existing on the surface, which supports plant life.
To an engineer, it is a material that can be:
built on: foundations of buildings, bridges
built in: basements, culverts, tunnels
built with: embankments, roads, dams
supported: retaining walls

## Slide 2
Soil Definition (Engineering)–“refers to all unconsolidated material in the earth’s crust, all material above bedrock”
•mineral particles (sands, silts, clays)
•organic material (topsoil, marshes) + air + water
Engineering Properties of Soils
–foundation for the project
–construction material (road embankments, earth dams)

## Slide 3
Soil Mechanics is a discipline of Civil Engineering involving the study of soil, its behavior and application as an engineering material.
Soils are formed from materials that have resulted from the disintegration of rocks by various processes of physical and chemical weathering.
The nature and structure of a given soil depends on the processes and conditions that formed it:
Breakdown of parent rock: weathering, decomposition, erosion.
Transportation to site of final deposition: gravity, flowing water, ice, wind.
Environment of final deposition: flood plain, river terrace, glacial moraine, lacustrine or marine.

## Slide 4
All soils originate, directly or indirectly, from different rock types.
Soils as they are found in different regions can be classified into two broad categories:
(1) Residual soils
(2) Transported soils
Transported Soils
Weathered rock materials can be moved from their original site to new locations by one or more of the transportation agencies to form transported soils.
Transported soils are classified based on the mode of transportation and the final deposition environment.

## Slide 5
(a) Soils that are carried and deposited by rivers are called alluvial deposits.
(b) Soils that are deposited by flowing water or surface runoff while entering a lake are called lacustrine deposits.
(c) If the deposits are made by rivers in sea water, they are called marine deposits.
(d) Melting of a glacier causes the deposition of all the materials scoured by it leading to formation of glacial deposits.
(e) Soil particles carried by wind and subsequently deposited are known as aeolian deposits.

## Slide 7
i. Soil texture
One aspect of the physical properties of soil, its texture, is described by the percent of particles in various size classes.
Particle size is the defining difference between sand, silt, and clay, but of course the size of the particle has much to do with its other properties.
Natural soils are nearly always mixtures of sand, silt, and clay particles, as well as organic matter and stones.
If a soil is composed of 40% sand, 35% silt, and 25% clay, it is called a loam.

## Slide 8
Clay- The smallest soil particle
Sand - The largest soil particle
Silt - An intermediate sized soil particle
Structure - The way individual soil particles are grouped together
Texture - A physical property of the soil referring to the relative percentages of sand, silt, and clay

## Slide 9: Light Soils vs Heavy Soils
Light Soils - sandy or coarse texture
Heavy Soils - clay or fine texture
Loamy Soils - medium textured
  more desirable characteristics usually associated with highly productive soils that are easier to manage

## Slide 10: Major Forms of Iron and Effect on Soil Color
Form Chemical Formula Color
Ferrous oxide FeO Gray
Ferric oxide
(Hematite) Fe2O3 Red
Hydrated ferric oxide (Limonite) 2Fe2O3 3H2O Yellow

## Slide 16
ENGINEERING PROPERTIES OF SOIL
The following properties of soil are taken into consideration while dealing with soil as a construction material.
Cohesion
Angle of internal friction
Capillarity
Permeability
Soil plasticity
Elasticity
Compressibility
Uniaxial Compressive Strength
Moisture Content & Available water capacity
Specific Gravity of Soils:

## Slide 17
Cohesion : It is the internal molecular attraction which resists the rupture or shear of a material.
Cohesion is derived in the fine grained soils from the water films which bind together the individual particles in the soil mass.
Cohesion is the property of the fine grained soil with particle size below 0.002 mm.
Cohesion of a soil decreases as the moisture content increases.
Cohesion is greater in well compacted clays and it is independent of the external load applied.

## Slide 18
Angle of Internal Friction: The resistance in sliding of grain particles of a soil mass depends upon the angle of internal friction.
It is usually considered that the value of the angle of internal friction is almost independent of the normal pressure but varies with the degree of packing of the particles, i.e. with the density.
The soils subjected to the higher normal stresses will have lower moisture contents and higher bulk densities at failure than those subjected to lower normal stresses and the angle of internal friction may thus change.
The true angle of internal friction of clay is seldom zero and may be as much as 26⁰ . The angle of internal friction fro granular soils may vary in between 28⁰ to 50⁰ .

## Slide 19
Capillarity : It is the ability of soil to transmit moisture in all directions regardless of any gravitational force.
Water rises up through soil pores due to capillary attraction.
The maximum theoretical height of capillary rise depends upon the pressure which tends to force the water into the soil, and this force increases as the size of the soil particles decreases.
The capillary rise in a soil when wet may equal as much as 4 to 5 times the height of capillary rise in the same soil when dry.
Coarse gravel has no capillary rise; coarse sand has up to 30 cm; fine sand and soils have capillary rise up to 1.2 m but dry sand have very little capillarity. Clays may have capillary rise up to 0.9 to 1.2 m but pure clays have very low value.

## Slide 20
Permeability : Permeability of a soil is the rate at which water flows through it under action of hydraulic gradient.
The passage of moisture through the inter- spaces or pores of the soil is called ‘percolation’.
Soils having porous enough for percolation to occur are termed ‘pervious’ or ‘permeable’, while those which do not permit the passage of water are termed ‘impervious’ or ‘impermeable’.
The rate of flow is directly proportional to the head of water. Permeability is a property of soil mass and not of individual particles. The permeability of cohesive soil is, in general, very small. Knowledge of permeability is required not only for seepage, drainage and ground water problems but also for the rate of settlement of structures on saturated soils.

## Slide 21
Soil plasticity : Soil plasticity is a property that enables the moist soil to change shape when some force is applied over it and to retain this shape even after the removal of the force from it.
The plasticity of soil depends on the cohesion and adhesion of soil materials.
Cohesion refers to the attraction of substances of like characteristics, such as, that of one water molecule for another.
Adhesion refers to the attraction of substances of unlike characteristics. Soil consistency depends on the texture and amount of inorganic and organic colloids, structure and moisture contents of soil.

## Slide 22
Elasticity : This elastic behavior is characteristic of peat.
A soil is said to be elastic when it suffers a reduction in volume (or is changed shape & bulk) while the load is applied, but recovers its initial volume immediately when the load is removed.
The most important characteristic of the elastic behavior of soil is that no matter how many repetitions of load are applied to it, provided that the stress set up in the soil do not exceed the yield stress, the soil does not become permanently deformed.

## Slide 23
Compressibility: Gravels, sands & silts are incompressible, i.e. if a moist mass of those materials is subjected to compression; they suffer no significant volume change.
Clays are compressible, i.e. if a moist mass of clay is subjected to compression, moisture & air may be expelled, resulting in a reduction in volume which is not immediately recovered when the compression load is withdrawn.
The decrease in volume per unit increase of pressure is defined as the compressibility of soil, and a measure of the rate at which consolidation proceeds is given by the ‘co- efficient of consolidation’ of the soil.
Compressibility of sand & silt varies with density & compressibility of clay varies directly with water content & inversely with cohesive strength.

## Slide 24
Uniaxial Compressive Strength (UCS) : Test Compressive strength is the capacity of a material to withstand axially directed compressive forces.
The most common measure of compressive strength is the uniaxial compressive strength (unconfined compressive strength).
Triaxial Compression : The triaxial compression test is a more sophisticated testing procedure for determining the shear strength of a soil.
The test involves a soil specimen subjected to an axial load until failure while also being subjected to confining pressure that approximates the in-situ stress conditions.

## Slide 25
Moisture Content & Available water capacity :
The moisture content (w) is defined as the ratio of the weight of water in a sample to the weight of solids. Available water capacity refers to the quantity of water that the soil is capable of storing for use by plants.
The capacity varies, depending on soil properties that affect the retention of water and the depth of the root zone. The most important properties are the content of organic matter, soil texture, bulk density, and soil structure.
Available water capacity is an important factor in the choice of plants or crops to be grown and in the design and management of irrigation systems.

## Slide 26
Specific Gravity of Soils:
The specific gravity of soil, Gs, is defined as the ratio of the unit weight of a given material to the unit weight of water.
Weight-Volume Relationships: In nature, soils are three-phase systems consisting of solid soil particles, water, an air (or gas). To develop the weight-volume relationships for a soil, the three phases can be separated.

## Slide 27
Soil strength tests are performed on high quality, relatively undisturbed in-situ specimens. However, it is difficult and frequently impossible to sample, transport, extrude and set- up testing for granular, cohesionless soils (Sand or Gravel) without excessively disturbing or completely obliterating the soil specimen.
It is difficult to obtain good strength values through lab testing of disturbed (remolded) specimens since the soil matrix (i.e., cohesion/ bonding of soil particles) is destroyed and the in-situ density and moisture content are very difficult to recreate.